## Slide 1: Exercises: DHT
Today’s goal: (implement and) run a p2p network using a distributed hash table.
DHT: Kademlia
Used in file sharing networks (BitTorrent) and blockchain (Ethereum).
pip install kademlia
Similar to Chord, but uses another distance function.
Nodes and values live in an m bit space.
distance(node1, node2) = (uint) XOR(id(node1), id(node2))
Keys and values are stored redundantly over the network.
Lookup operation takes steps.
Notes: https://medium.com/coinmonks/a-brief-overview-of-kademlia-and-its-use-in-various-decentralized-platforms-da08a7f72b8f

## Slide 2: Kademlia
Each node keeps a routing table where lists of nodes are stored.
Routing table has entries
  i-th entry includes those nodes that have the previous i-1 bits equal to the node that is being sougth.
  The further into the list, the closer the nodes in the list are.
Lookup first using the closest nodes in the list.
If key not present, use nodes further away.
… until key found.

## Slide 3: Kademlia

## Slide 4: Exercises
Pull DS_Examples
DS_Examples/p2p/p2pnode_exercise.py
Implement a coroutine (async) that waits for user input and implements two operations
  Set the value for a given key (Server.set)
  Get the value of a given key (Server.get)
  Hint: Use the aioconsole package and the ainput function

## Slide 5: Execises
Modify the program so that in case that no parameters are given for “join”, the IP address of the neighbour will be read form the P2P_REMOTE_HOST environment variable
  If this variable is empty, then a “create” and not a “join” will be made
  Hint: Environment variables are stored in the os.environ dictionary
Write a Dockerfile that exposes the default port

## Slide 6: Docker: Advanced Networking
We will create a user network for our p2p network
Types of networks
  Bridge: default type
    Containers in a bridge network can communicate between themselves, but not with containers in other bridge networks
    User-created bridge networks provide name resolution
host
bridge0
user-bridge
container0
container1
container2
container3
container4

## Slide 7: Docker: Advanced Networking
Bridge networks can only communicate inside the same Docker daemon
Overlay networks: containers can communicate with other Docker daemons
Macvlan: can assign MAC addresses to containers
None: container runs isolated
Third party plugins: custom functionality

## Slide 8: Exercises
Create your own p2p network (p2p_setup.md) and set and get values on the network